## Slide 1
DIGITAL LOGIC DESIGN PROJECT
4-Bit Binary Arithmetic Calculator Using Combinational Logic
Combinational 4-Bit Adder and Subtractor Architecture
TEAM MEMBERS
2620030686 - K. Mokshagna Reddy 2620030213 - Shreyash 2620040121 - Shiva Shreyas 2620040058 - Deepak Vemulapalli
PROJECT GUIDE
Dr. Venkanna Isampalli
DEPARTMENT & SESSION
Freshman Engineering | KLEF 2026–27

## Slide 2
BACKGROUND & MOTIVATION
Introduction
Core Logic Foundation
Binary arithmetic forms the essential computational foundation for modern microprocessors and Arithmetic Logic Units (ALUs).
While advanced CPUs utilize integrated sequencers, fundamental addition and subtraction are executed strictly via combinational logic gates.
Hardware-Direct Processing
This project constructs a standalone 4-bit adder-subtractor without reliance on microcontrollers or software programming.
It demonstrates practical digital logic design by processing inputs instantly using hardware gate propagation.

## Slide 3
PROJECT GOALS
Objectives
01
Circuit Design
Design a 4-bit binary calculator for addition and subtraction using fundamental logic gates.
02
Shared Hardware
Implement 2's complement arithmetic to enable subtraction through shared adder circuits.
03
Control Sequence
Utilize XOR mode control and flip-flop staging for seamless operation switching.
04
Verification
Simulate and test internal carry propagation and output flags across all 4-bit cases.

## Slide 4
ACADEMIC ALIGNMENT
Course Outcomes (COs)
CO1
Apply Boolean algebra and logic gates to digital circuits.
CO2
Design combinational circuits for a given specification.
CO3
Use flip-flops and counters for sequential control.
CO4
Simulate, test, and troubleshoot digital circuits.
CO5
Explain the real-time application of digital electronics.

## Slide 5
HARDWARE SPECIFICATIONS
Components Required
Power & Clock
5V DC Power Supply
555 Timer IC / Clock Pulse Generator
Integrated Circuits
7483 4-Bit Binary Adder IC
7486 Quad 2-Input XOR IC
JK/D Flip-Flops (7476 / CD4027)
Basic Logic Gates
7408 AND Gate IC
7432 OR Gate IC
7404 NOT Gate IC
Sequential Units
IC 7493 Binary Counter (Optional)
Indicators
Red, Yellow & Green Output LEDs
Prototyping
220Ω Resistors, Breadboard & Wires

## Slide 6
SYSTEM ARCHITECTURE
Block Diagram & Logisim Circuit
Circuit Flow: Cascaded 4-bit full adders combined with XOR inversion logic for addition and 2's complement subtraction.

## Slide 7
OPERATIONAL MECHANICS
Circuit Working
Addition Mode
Mode = 0
• XOR gates pass bit vector $B$ unchanged.
• Initial carry-in $C_{in} = 0$.
• Circuit performs standard binary addition: $S = A + B$.
Subtraction Mode
Mode = 1
• XOR gates invert input $B$ to 1's complement ($\bar{B}$).
• Mode line supplies $C_{in} = 1$ to LSB stage.
• Circuit executes 2's complement subtraction: $A + \bar{B} + 1 = A - B$.
Flag Handling
Carry & Borrow
• $C_{out}$ from MSB stage drives carry output LED.
• Indicates unsigned arithmetic overflow in addition.
• Serves as borrow status flag during subtraction mode.

## Slide 8
Mode (M) | A [3:0] | B [3:0] | Effective B Input | Cin | Result Sum [3:0] | Cout / Borrow
0 (ADD) | 0101 (5) | 0011 (3) | 0011 | 0 | 1000 (8) | 0
0 (ADD) | 1100 (12) | 0101 (5) | 0101 | 0 | 0001 (17-16) | 1 (Carry Set)
1 (SUB) | 0111 (7) | 0010 (2) | 1101 (~B) | 1 | 0101 (5) | 1 (No Borrow)
1 (SUB) | 0100 (4) | 0110 (6) | 1001 (~B) | 1 | 1110 (-2 in 2's Comp) | 0 (Borrow Needed)
FUNCTIONAL VERIFICATION
Truth Table

## Slide 9
BOOLEAN FORMULATIONS
Logic Design
Full Adder Stage i Equations
Gate Mapping
• XOR Gates (7486): Mode inversion array and sum computation.
• AND Gates (7408): Partial product carry generation.
• OR Gates (7432): Carry propagation network assembly.
B_effective_i = B_i ⊕ Mode
Sum_i = A_i ⊕ B_effective_i ⊕ C_i
C_(i+1) = (A_i · B_eff_i) + (C_i · (A_i ⊕ B_eff_i))

## Slide 10
TESTING & VALIDATION
Simulation / Implementation
Software Tools
Simulated using Logisim, Multisim, and Tinkercad digital test benches.
Hardware Setup
Breadboard prototype wired using standard 74xx series ICs and current-limiting resistors.
Verification Sequence
Validated all 16 addition and subtraction corner cases against theoretical truth tables.

## Slide 11
SYSTEM STRENGTHS
Advantages
Hardware Efficiency
Low-cost execution with minimal chip count using basic 74xx series ICs.
Zero Software Dependency
Pure hardware logic operation without requiring firmware, microcontrollers, or clocks.
Educational Clarity
Provides transparent insight into low-level ALU operation and binary arithmetic.
Modularity
Cascading structure allows simple expansion to 8-bit, 16-bit, or wider word sizes.

## Slide 12
DESIGN CONSTRAINTS
Limitations
Propagation Delay
Ripple carry propagation introduces gate delays as word size scales up.
Fixed Bit-Width
Restricted to 4-bit operands (-8 to +7 signed / 0 to 15 unsigned range).
Function Boundary
Handles addition and subtraction only; multiplication requires extra external logic.

## Slide 13
HORIZON & EXTENSIONS
Applications & Future Scope
Real-World Applications
• Core building block for CPU Arithmetic Logic Units (ALUs).
• Educational digital logic demonstration platform in academic labs.
• Embedded hardware address counters and incrementers.
Future Enhancements
• Upgrade to Carry Lookahead Adders (CLA) to reduce propagation delay.
• Expand functionality to support bitwise AND, OR, and XOR operations.
• Interfacing with 7-segment displays for direct decimal output readout.

## Slide 14
SUMMARY
Conclusion
Project Synthesis
• A 4-bit binary calculator was successfully designed and verified using basic logic gates and full adder stages.
• The system seamlessly executes addition and 2's complement subtraction using a single XOR mode control line.
• Provides a complete foundational model for hardware-level arithmetic computation in modern computer architecture.

## Slide 15
DOCUMENTATION & DELIVERABLES
GitHub Repository
Repository Details
Link: https://github.com/V-Shreyash213/DDCA-Project
Contents: Schematics, Logisim files, project report, presentation, and setup README.
Team Contributions
• Circuit design and schematic drafting.
• Software simulation and truth table validation.
• Breadboard implementation and slide deck preparation.

## Slide 16
Thank You
Questions & Discussion